## Slide 1: On the Vulnerability of the Proportional Fairness Scheduler to Retransmissions Attacks
Udi Ben-Porat ETH Zurich Switzerland
Anat Bremler-Barr IDC Herzliya Israel
Hanoch Levy Tel-Aviv University Israel
Bernhard Plattner ETH Zurich Switzerland
INFOCOM 2011

## Slide 2: Wireless Scheduling
Players: Base Station (BS) and Clients
Time is divided to time slots
In each slot, data is sent to one user only
Clients have variable channel conditions
The scheduler selects a client for transmission based on the reported channel condition of the users
Scheduler’s objectives:
  Good overall throughput performance of the system
  Fairness among users (avoid starvation)

## Slide 3: PROBLEM & Contributions
The Common Scheduler – Proportional Fairness (PFS)
  Fair & Efficient (widely studied and deployed)
PROBLEM: Retransmission policy overlooked
ISSUE: Malicious Users can Downgrade Performance
Contributions:
  Expose vulnerability of the PFS wireless scheduler
  Examine and Analyze potential solutions
  Propose a solution that maintains fairness and immune to attacks
* All claims in this work are analytically proved and backed up by simulations.

## Slide 4: Proportional Fairness Scheduler (PFS) – User Info
Vi(t)
Ri(t)
Ai(t)
Throughput Average (until t)
Priority Value
Rate (at time t)
The user with the highest priority is scheduled

## Slide 5: Proportional Fairness Scheduler (PFS)
Base Station
DATA
User 1
User 2
V1(t) = 2
Priority Value
Rate
R1(t) = 400 b/s
R2(t) = 300 b/s
Rate
V2(t) = 3
Priority Value
A1(t) =200
A2(t) =100
Throughput Average

## Slide 6: Throughput Average Ai(t)
Throughput Average update – “Admitted Average”:
  1ircv(t) = 1 if user i received a transmission in time t (o/w 0)
Ri(t) is the “price” the user “pays” per transmission
Higher “price”  Higher Ai(t)  Harder to “win” future time slots
Ai(t+1) = (1- ε)Ai(t) + ε1ircv(t)Ri(t)

## Slide 7: Frame Losses and Retransmissions
DATA
Sorry, I didn’t get it.
Send again please!
OK, just a moment
Hey!
What about us?
Hmm…
1. When to retransmit a lost frame?
  Should pending retransmissions get the highest priority?
2. What is the real received data rate?
  Due to losses, Ri(t) does not reflect the real rate to the user

## Slide 8: Frame Losses and Retransmissions
When to retransmit a lost frame?
  „Fast Ret.“
    Retransmit immediately (ignore other users)
  „Slow Ret.“
    Some other user has higher priority? - Delay retransmission
Effective Rate - Rei(t)
  Effective Rate = The rate the user is expected to receive
Example: Ri(t) = 200 Kb/s , Loss Prob. = 0.2  Rei(t) = 160 Kb/s
    Vi(t) = Rei(t) / Ai(t)

## Slide 9: Frame Losses and Retransmissions
NEW DATA
200
Kb/slot
Regular User |  |  | 
Time | Data | ack/nak | Payment
1 |  |  | 
2 |  |  | 
101000100101010110111000
= 0
200Kb
0 Kb
t = 1
Rate selected: 200 b/s
Prob. For frame loss = 0.2
Rei(t) = 200(1-0.2)=160 b/s
Base Station
User i

## Slide 10: Frame Losses and Retransmissions
RETRANSMISSION
200
Kb/slot
t = 2
= 200
200 Kb
200Kb
Regular User |  |  | 
Time | Data | ack/nak | Payment
1 |  |  | 
2 |  |  | 
101000100101010110111000
200Kb
0 Kb
Base Station
User i
Rate selected: 200 b/s
Prob. For frame loss = 0.2
Rei(t) = 200(1-0.2)=160 b/s

## Slide 11: Our Contributions
Retransmissions Scheduling – Vulnerable!
Propose Immune & Fair solutions
 | Fast Ret. |  | Slow Ret. | 
Averaging Method | Immune | Fair | Immune | Fair
Admitted Avg. (original) |  |  |  | 
Transmission Avg. |  |  |  | 
Effective Avg. |  |  |  | 
Initial Effective Avg. |  |  |  | 

## Slide 12: Admitted Average – Malicious Attack
NEW DATA
200
Kb/slot
= 0
Malicious user |  |  | 
Time | Data | Ack/Nak | Payment
1 |  |  | 
2 |  |  | 
3 |  |  | 
4 |  |  | 
5 |  |  | 
101000100101010110111000
200Kb
0 Kb
Rate selected: 200 b/s
Prob. For frame loss = 0.2
Rei(t) = 200(1-0.2)=160 b/s
Base Station
Malicious
User

## Slide 13: Admitted Average – Malicious Attack
RETRANSMISSION
200
Kb/slot
= 200
Malicious user |  |  | 
Time | Data | Ack/Nak | Payment
1 |  |  | 
2 |  |  | 
3 |  |  | 
4 |  |  | 
5 |  |  | 
101000100101010110111000
0 Kb
200Kb
0 Kb
200Kb
200Kb
200Kb
200Kb
0 Kb
0 Kb
200 Kb
Malicious
User
Base Station
Rate selected: 200 b/s
Prob. For frame loss = 0.2
Rei(t) = 200(1-0.2)=160 b/s

## Slide 14: Retransmissions Attack – Simulation Results
  Example:
    10% are malicious
    # of retransmissions are limited to Lmax =10
    40% time share loss for every regular user
  X – Percentage of malicious users
  Y – Time share loss for regular users

## Slide 15: Results
 | Fast Ret. |  | Slow Ret. | 
Averaging Method | Immune | Fair | Immune | Fair
Admitted Avg. (original) |  |  |  | 

## Slide 16: Sol #1 – Transmission Average
Sol #1 - “Pay” for every transmitted frame
1isnd(t) = 1 if a frame was sent (o/w 0)
Ai(t+1) = (1- ε)Ai(t) + ε1isnd(t)Ri(t)

## Slide 17: Immunity of “Transmission Average”
Malicious user |  |  | 
Time | Data | Ack/Nak | Payment
1 |  |  | 
2 |  |  | 
3 |  |  | 
4 |  |  | 
5 |  |  | 
101000100101010110111000
200Kb
200Kb
200Kb
200 Kb
200 Kb
200Kb
200 Kb
200Kb
200 Kb
200 Kb
Total “Payment”: 1000Kb
200 Kb
200Kb
Regular User |  |  | 
Time | Data | Ack/Nak | Payment
1 |  |  | 
2 |  |  | 
101000100101010110111000
200Kb
200 Kb
Total “Payment”: 400Kb
The Scheduler is immune to attack
What about Fairness?

## Slide 18: Transmission Average – Distorted Fairness
2 Regular users |  |  |  |  | Results* | 
User | Effective Rate Rei(t) | Rate Ri(t) | Frame Loss Prob. | “Payment” per bit | Time Share | Download Speed
A | 100 b/s | 200 b/s | 0.5 | 1/(1-0.5) = 2 | 38% | 38 b/s
B | 90 b/s | 100 b/s | 0.1 | 1/(1-0.1) = 1.1 | 62% | 55.8 b/s
User A has a better channel condition than User B, but still…
  …gets smaller time share
  …receives less throughput
This stands against any notion of fairness!
* Long run results. Derived from an analytical result proved in the paper.

## Slide 19: Results
 | Fast Ret. |  | Slow Ret. | 
Averaging Method | Immune | Fair | Immune | Fair
Admitted Avg. (original) |  |  |  | 
Transmission Avg. |  |  |  | 

## Slide 20: Sol #2 – Effective Average
“Pay for what I expect you to receive”
Immune: Malicious has to pay for excessive ret.
Fair: Ai(t+1) = The throughput user i actually received
Ai(t+1) = (1- ε)Ai(t) + ε1isnd(t)Rei(t)

## Slide 21: Effective Average (Sol. #2)
Regular user |  |  |  | 
Time | Rei(t) Effective Rate | Data | ACK/NAK | Payment
1 |  |  |  | 
3 |  |  |  | 
101000100101010110111000
300 b
300 b
150 b/s
150 b/s
150 b/s
150 b/s
Regular user: 300 b/s, 2 transmissions
Rate selected: 300 b/s
Frame loss Probability = 1/2
Rei(t) = 150 b/s

## Slide 22: Effective Average (Sol. #2) for Fast retransmissions
Malicious user |  |  |  | 
Time | Rei(t) Effective Rate | Data | ACK/NAK | Payment
1 |  |  |  | 
2 |  |  |  | 
3 |  |  |  | 
Malicious user: 170 b/s, 3 transmissions
101000100101010110111000
300 b
10 b/s
150 b/s
10 b/s
Rate selected: 300 b/s
Frame loss Probability = 1/2
Rei(t) = 150 b/s
10 b/s
150 b/s
10 b/s
Regular user: 300 b/s, 2 transmissions

## Slide 23: Results
 | Fast Ret. |  | Slow Ret. | 
Averaging Method | Immune | Fair | Immune | Fair
Admitted Avg. (original) |  |  |  | 
Transmission Avg. |  |  |  | 
Effective Avg. |  |  |  | 

## Slide 24: Sol #3 – Initial Effective Rate (for Fast Ret.)
Initial Effective Rate (sol #3)
  Every retransmission costs as the first transmission
  Fi (t)= The last time slot where user i received an initial trans.
Choosing fast retransmission is preferred when:
  Small changes in channel conditions between slots
    Time slots are very short
    Channel condition is stable
  The preferred user in time t, is probably also the one in t+1
Ai(t+1) = (1- ε)Ai(t) + ε1isnd(t) Rei(Fi (t))

## Slide 25: Results
 | Fast Ret. |  | Slow Ret. | 
Averaging Method | Immune | Fair | Immune | Fair
Admitted Avg. (original) |  |  |  | 
Transmission Avg. |  |  |  | 
Effective Avg. |  |  |  | 
Initial Effective Avg. |  |  |  | 

## Slide 26: Conclusions
The Proportional Fairness Scheduler is vulnerable to retransmissions attacks
  Both for Fast and Slow retransmission methods
We proposed modifications to PFS
  Proved to be proportional fair and immune to ret. attacks
  Both for Fast and Slow retransmission methods

## Slide 27: Questions?